## Slide 1: High Pressure Acid Leach
At high leach temperatures, typically between 200~270°C, refractory oxides and silicates are decomposed, liberating metals to solution as described by the general equation below, where M=Ni, Co, Cu, Fe, Mg, Mn and Zn.
MO + H2SO4 ⇒ MSO4 +H2O

## Slide 2: Extraction Theory
2
Initial condition:
Diffusion of H2SO4 to ore
particle and adsorption on
FeO(OH) and NiO surface
Chemical reaction of H2SO4
w/ FeO(OH) and NiO particles
at autoclave operating T and P
1
Ore
Particle
NiO
FeO(OH)
H2SO4
NiO particles dispersed within goethite

## Slide 3: Extraction Theory
2
3
After reaction:
Hydrolysis of FeO(OH) to
Fe2O3 at given T and P.
Dissolution of Ni++ ions to
to form NiSO4 solution
Unreacted NiO particles
remaining in Fe2O3 residue
1
Ore
Particle
H++
Ni++
SO4 --
Fe2O3
NiO