## Slide 1: EMERGENCY SHUT DOWN (ESD) Basic Information for Field Operators
List of ESD
Pump Auto-Start Sequence after Power Failure Recovery
1. Order of Priority for Auto Start
2. Pump Auto-Start List
III. Safety Instrumented System(SIS)
IV. Operators Actions when ESD occur
TNH-200-101 (5)

## Slide 2: I. List of ESD
No. | Logic Block | Description
1 | 102/202 – UZ – 600 | Autoclave Shutdown
2 | 102/202 – UZ – 620 | Steam Shutdown
3 | 102/202 – UZ – 660 | Acid Shutdown
4 | 102/202 – UZ – 680 | HP Air Shutdown
5 | 106 – UZ – 800 | MS Plant Shutdown
6 | 106 – UZ – 810 | H2S Vent Scrubber (SR02) Shutdown
7 | 106 – UZ – 820 | Scrubber Shutdown (SR03)

## Slide 3: I.1 Autoclave Shutdown
ESD CAUSE | ESD Action | KBS Action
Autoclave Compressor #7 Level HH | Steam Shutdown Acid Shutdown HP Air Shutdown | LT/MT/HT Feed Pump Stop Autoclave Feed Pump Stop
HT Heater Overhead Pressure HH |  | 
Autoclave HH Pressure |  | 
ESD Push Button on Aux Console |  | 
Power Failure |  | 
Note: To notify Operators, Autoclave Shutdown HORN at the Area will be initiated.

## Slide 4: I.2 Autoclave Steam Shutdown
ESD CAUSE | ESD Action
HP Steam Blowback Vessel Level HH | Autoclave Comp. #1, #2, & #5 Steam Valve CLOSE Steam Isolation Valve CLOSE
Autoclave Steam Header Pressure HH | 
Autoclave Shutdown | 
ESD Push Button on Aux Console | 
Electric Power Failure | 

## Slide 5: I.3 Acid Shutdown
ESD CAUSE | ESD Action
Autoclave Comp.#1 Level LL | Acid Pump TRIP Autoclave Comp.#1AB Acid Valves CLOSE Acid Line N2 Purging START Acid feed pump suction valves CLOSE
Autoclave Comp.#7 Level LL | 
Autoclave Comp.#1AB Acid Feed Flow LL | 
Autoclave Comp.#1AB Acid Feed Pressure LL | 
Acid Tank Level LL | 
Autoclave Shutdown | 
ESD Push Button on Aux Console | 
Electric Power Failure | 

## Slide 6: I.4 HP Air Shutdown
ESD CAUSE | ESD Action
Autoclave HP Air Header Pressure HH | HP Air Isolation Valve CLOSE HP Air Control Valve CLOSE
Autoclave HP Air Header Pressure LL | 
Autoclave Shutdown | 
ESD Push Button on Aux Console | 
Electric Power Failure | 

## Slide 7: I.5 MS Plant Shutdown
ESD CAUSE | ESD Action
MS Reactors Pressure HH | MS Seed Pump TRIP H2S Gas Compressor TRIP Vacuum Pump TRIP MS Feed Pump TRIP H2S Feed Valve to MS Reactors CLOSE MS Seed Valve CLOSE MS Reactor #4 Discharge Valve CLOSE Steam Valve to MS Feedline CLOSE H2S Shutdown
MS Reactors Level HH | 
H2S Gas Compressor Discharge Pressure HH | 
Instrument Air Pressure LL | 
Nitrogen Pressure LL | 
Electric Power Failure | 
ESD Push Button on Aux Console | 

## Slide 8: I.6 H2S Vent Scrubber (SR02) Shutdown
ESD CAUSE | ESD Action
Pre-scrubber Level LL | MS Seed Pump TRIP H2S Gas Compressor TRIP H2S Vacuum Pump TRIP MS Feed Pump TRIP H2S Feed Valve to MS Reactors CLOSE MS Seed Valve CLOSE MS Reactor #4 Discharge Valve CLOSE Steam Valve to MS Feedline CLOSE H2S Shutdown H2S gas Feed Valve to DeZn Reactors CLOSE DeZn Reactors Vent Valves CLOSE MS Reactors Vent Valves CLOSE NTRL Overflow Pump TRIP Polishing Filter Feed Pumps TRIP Pregnant Liquor Recovery Pump TRIP
Vent Scrubber Level LL | 
Vent Scrubber O2 Concentration HH | 
Vent Scrubber Pressure HH | 
Vent Scrubber Fan Stop | 
Vent Scrubber H2S Concentration HH | 
Vent Scrubber Circulation Pump Stop | 
Pre-scrubber Circulation Pump Stop | 
Instrument Pressure LL | 
Nitrogen Pressure LL | 
Electric Power Failure | 
Vent Scrubber Shutdown Push Button | 

## Slide 9: I.7 Scrubber (SR03) Shutdown
ESD CAUSE | ESD Action
SR03 Level LL | MS Seed Pump TRIP H2S gas Compressor TRIP H2S Vacuum Pump TRIP MS Feed Pump TRIP H2S Feed Valve to MS Rxts CLOSE Seed Valve to MS Feedline CLOSE MS Rxt #4 discharge valve CLOSE Steam Valve to MS Feedline CLOSE H2S Shutdown H2S Feed Valve to DeZn Rxts CLOSE MS Rxts Vent Valves CLOSE NTRL Thickener Overflow Pump TRIP Polishing Filter Feed Pump TRIP Pregnant Liquor Recovery Pump TRIP H2S Destruction Blower TRIP
SR03 H2S Concentration HH | 
SR03 Fan Stop | 
SR03 Circulation Pump Stop | 
Instrument Air LL | 
Nitrogen Pressure LL | 
Electric Power Failure | 
SR03 Shutdown Push Button | 

## Slide 10: II. Pump Auto-Start Sequence after Power Failure
Power Failure Interlock is provided for all motors.
When Power Failure is due to Steam Turbine
Generator Shutdown, Emergency Generator will
Start.
When power is restored, motors with auto-start
sequence will automatically run the with order of
priority.

## Slide 11: II.1 Order of Priority for Auto-Start
Priority | Time Delay | Description
1 | 0 | All small size motors
2 | 5 | 1st Pump of Cooling Water Pump
3 | 10 | 2nd Pump of Cooling Water Pump
4 | 20 | Clarified Water Pump
5 | 25 | Selected Vent Scrubber Fan
6 | 30 | Cooling Tower for MS
7 | 40 | 1st Compressor of Instrument Air
8 | 50 | 2nd Compressor of Instrument Air

## Slide 12: II.2 Pump Auto-Start List (1)
System | Equipment* | Description
HPAL Scrubber | 102/202PU08AB 102/202PU16AB | Scrubber Seal Tank Discharge Pump Scrubber Feed Water Booster Pump
Utility Clarified Water Pump | 513PU01ABC | Clarified Water Pump
Filtrated Water Pump | 513PU02ABC | Filtrated Water Pump
MS Scrubbers | 106PU41AB | H2S Scrubber(SR02) Recycle Pump
 | 106FN01AB | H2S Vent Scrubber Fan
 | 106PU51AB | Scrubber Water Re-circulation Pump
 | 106FN02AB | Scrubber(SR03) Fan
* Selected Pump/Fan will RUN

## Slide 13: II.2 Pump Auto-Start List (2)
System | Equipment* | Description
H2S Vent Scrubber | 106PU00AB | Pre-Scrubber Recycle Pump
HPAL Agitator Seal | 102/202PU12AB 102/202PU14AB | HPAL AG Flush Water Pump HPAL AG Seal Water Pump
HPAL Pump Seal | 102PU15AB 102PU15AB Aux | Seal Water Pump Seal Water Pump Pre-Lube Oil
FNTRL Pump Seal | 108PU21AB 108PU21AB Aux | Seal Water Pump Seal Water Pump Pre-Lube Oil
Pump Mech Seal | 513PU03AB | HP Gland Water Pump
H2S Vac Seal | 106VB01AB Aux | H2S Vacuum Pump Aux Seal
H2S Comp Seal | 106CP01AB Aux | H2S Compressor Aux Seal
* Selected Pump/Fan will RUN

## Slide 14: II.2 Pump Auto-Start List (3)
System | Equipment* | Description
Cooling Tower | 530CT31 530PU31ABC | Cooling Tower for MS Cooling Tower Pump
H2S Plant | 109/209BW01AB | Reactor Flange Box Extraction Fan
 | 109/209BW02 | Gas Cooler Room Extraction Fan
 | 109/209BW03 | Knock-out Drum Room Extraction Fan
 | 109/BW04AB | Containment Rooms Extraction Fan**
 | 109PU21AB | Process Gas Scrubber Circulation Pump
 | 109PU22AB | Emergency Gas Scrubber Circulation Pump
 | 109PU23AB | Leak Gas Scrubber Circulation Pump
Utility | 521CP01ABCD | Air Compressor**
* Selected Pump/Fan will RUN
** Both will RUN

## Slide 15: III. Safety Instrumented System (SIS)
This system safeguards and ensures the safety of the personnel,
environment and process whenever failures on H2S Plant operation
are encountered.
Should there be a detection of discrepancy of process value and the system’s set point value, the consequent Safety Instrumented Function will trip and shall initiate a timely actions.
  Primary Action- required process design to directly remove detected hazard.
  Secondary Action- follow up process responses that can be used to bring the process to a stop.

## Slide 16: SIS List(1)
No. | Logic Block/SIF | Description
1 | UZ- 400 | Manual Pushbutton Plant Box-in
2 | UZ- 410 | Quench Column High Differential Pressure Trip
2 | UZ- 420 | Manual Pushbutton Depressurize Plant
4 | UZ- 430 | MS Plant Available
5 | UZ- 450 | H2S Concentration HH on Emergency Gas Scrubber Discharge
6 | UZ- 460 | H2S Gas HH on Gas Leak Scrubber Discharge
7 | UZ- 470 | Utilities Unavailable
8 | SIF-001 | Emergency Gas Scrubber(109SR02) Unavailable
9 | SIF- 003 | Gas Leak Scrubber(SR03) Unavailable
10 | SIF-026 | Process Gas Scrubber(109SR01) HH Pressure

## Slide 17: SIS List(2)
No. | Logic Block/SIF | Description
11 | SIF- 059 | H2S Concentration HH on Emergency Gas Scrubber(109SR02) Discharge
12 | SIF- 060 | H2S Concentration HH on Gas Leak Scrubber(109SR03) Discharge
13 | SIF- 153A/253A | Gas Cooler Room Gas Detector HH Trip
14 | SIF- 153B/253B | Knockout Drum Gas Detector HH Trip
15 | SIF- 153C/253C | Quench Column Room Gas Detector HH Trip
16 | SIF- 153G | Area H2S Gas Detector HH Trip

## Slide 18: III.1 UZ-400 Manual Pushbutton Plant Box-in
Purpose: Executes Emergency Shutdown Sequence of H2S Plant by stopping
the input of H2 gas and molten sulfur to the H2S reactor and stopping
the draw-out of H2S gas from the H2S header.
Cause of SIS | SIS Action
Activating manual pushbutton in the H2S Emergency Shutdown Console | CLOSE Reactor Feed Valve CLOSE Hydrogen Supply Valve CLOSE Nitrogen Supply Valve CLOSE Reactor Supply Sulfur Valve CLOSE H2S Gas Product Line Valves CLOSE H2S Gas from Knock-out Drum Depressurizing CLOSE Valve to Gas Scrubber System CLOSE H2S Gas Sampling System Isolation Valve

## Slide 19: III.2 UZ-410 Quench Column High Differential Pressure Trip
Purpose: Prevents potential hazard of overpressure of the reactor which could
result to possible release of H2S gas to the environment, major plant
damage and lost production.
Cause of SIS | SIS Action
HH differential pressure reading in the lower packing section of Quench Column; or HH differential pressure reading in the upper packing section of Quench Column | Primary Action CLOSE Reactor Feed Valve CLOSE Hydrogen Supply Valve Secondary Action CLOSE Nitrogen Supply Valve CLOSE Reactor Supply Sulfur Valve CLOSE Gas Product Line Valve CLOSE Gas from Knock-out Drum Depressurizing CLOSE Valve to Gas Scrubber System CLOSE Gas Sampling System Isolation Valve

## Slide 20: III.3 UZ-420 Manual Pushbutton Depressurize Plant
Cause of SIS | SIS Action
Plant Box-in in Manual Pushbutton Emergency Gas Scrubber Unavailable. | CLOSE Reactor Feed Valve CLOSE Hydrogen Supply Valve CLOSE Nitrogen Supply Valve CLOSE Reactor Supply Sulfur Valve CLOSE H2S Gas Product Line Valves CLOSE H2S Gas from Knock-out Drum Depressurizing CLOSE Valve to Gas Scrubber System CLOSE H2S Gas Sampling System Isolation Valve
Purpose: Executes Emergency Shutdown and Plant Depressurization Sequence
of H2S Plant by stopping the input of H2 gas and molten sulfur to the
H2S reactor and stopping the draw-out of H2S gas from the H2S header.

## Slide 21: III.4 UZ-430 MS Plant Unavailable
Purpose: Execute Emergency Shutdown Sequence of both H2S Plant Train 1& 2
by stopping the draw-out of H2S gas and eventually stopping the inputs
of hydrogen and sulfur to the H2S reactor.
Cause of SIS | SIS Action
MS Plant ESD | Primary Action CLOSE H2S gas Product Line Valves Secondary Action CLOSE Reactor Feed Line Valve CLOSE Hydrogen Supply Valve CLOSE Nitrogen Supply Valve CLOSE Reactor Supply Sulfur Valve CLOSE Gas from Knock-out Drum Depressurizing CLOSE Valve to Gas Scrubber System CLOSE H2S Gas Sampling System Isolation Valve
H2S Vent Scrubber ESD | 
Scrubber ESD | 

## Slide 22: III.5 UZ-450 H2S Concentration HH on Emergency Gas Scrubber Discharge
Purpose: Initiates Emergency Gas Scrubber Shutdown when two Gas Analyzers
reading are HH, thus, preventing the discharge of high concentration to
environment.
Cause of SIS | SIS Action
Gas Analyzers reading HH=5ppm *Note: Operators are notified through Plant Alarm/Horn | Primary Action CLOSE Gas Scrubber System Inlet Valves Secondary Action CLOSE Reactor Feed Line Valve CLOSE Hydrogen Supply Valve CLOSE Nitrogen Supply Valve CLOSE Reactor Sulfur Supply Valve CLOSE Gas Product Line Valves CLOSE from Knock-out Drum Depressurizing CLOSE Valve to Gas Scrubber System CLOSE Gas Sampling System Isolation Valve

## Slide 23: III.6 UZ-460 H2S Gas HH on Gas Leak Scrubber Discharge
Purpose: Initiates Gas Leak Scrubber Shutdown when two Gas Analyzers reading
are HH, thus, preventing the discharge of high concentration to
environment.
Cause of SIS | SIS Action
Gas Analyzers reading HH=5ppm *Note: Operators are notified through Plant Alarm/Horn | Primary Action CLOSE Gas Leak Scrubber Inlet Valves Secondary Action CLOSE Reactor Feed Line Valve CLOSE Hydrogen Supply Valve CLOSE Nitrogen Supply Valve CLOSE Reactor Sulfur Supply Valve CLOSE Gas Product Line Valves CLOSE from Knock-out Drum Depressurizing CLOSE Valve to Gas Scrubber System CLOSE Gas Sampling System Isolation Valve

## Slide 24: III.7 UZ-470 Utilities Unavailable
Purpose: Prevent H2S Plant from operating whenever the Plant Utilities is
unavailable.
Cause of SIS | SIS Action
Instrument Air Pressure LL | Secondary Action CLOSE Reactor Feed Line Valve CLOSE Hydrogen Supply Valve CLOSE Nitrogen Supply Valve CLOSE Reactor Sulfur Supply Valve CLOSE Gas Product Valves CLOSE Gas fom Knock-out Drum Depressurizing CLOSE Valve to Gas Scrubber System CLOSE Gas Sampling System Isolation Valve
High Purity Nitrogen Pressure LL | 
Low Purity Nitrogen Pressure LL | 
Electric Power Failure | 
Hydrogen Buffer Vessel Pressure LL | 

## Slide 25: III.8 SIF 001 Emergency Gas Scrubber (SR02) Unavailable
Purpose: Isolate Emergency Gas Scrubber in the event of level controller/
circulation pump failure and blockage of scrubber packing.
Cause of SIS | SIS Action
Caustic Flow Upper Inlet LL | Primary Action CLOSE Emergency Gas Scrubber Inlet Valve (109HV056)
Caustic Flow Lower Inlet LL | 
Scrubber Level LL | 
Scrubber Packing PDI HH | 
Scrubber Inlet Pressure HH | 

## Slide 26: III.9 SIF 003 Gas Leak Scrubber (SR03) Unavailable
Purpose: Isolate Gas Leak Scrubber to prevent release of high concentration
H2S waste gas.
Cause of SIS | SIS Action
Scrubber Caustic Flow LL | Primary Action CLOSE Gas Leak Scrubber Inlet Valve (109HV059) STOP Fume Extraction Fan
Scrubber Level LL | 
Scrubber Packing PDI HH | 

## Slide 27: III.10 SIF-026 Process Gas Scrubber HH Pressure
Purpose: Detects a high pressure in the Process Gas Scrubber(109SR01) and
open a direct path to the Emergency Gas Scrubber(109SR02),thus, preventing equipment damage.
Cause of SIS | SIS Action
109SR01 Inlet Pressure HH | OPEN 109SR01 Divert Valve CLOSE 109SR01 Inlet Valve
109SR01 Differential Pressure HH | 
Alarm to notify Operators
  Annunciation Lamp is energized at H2S Emergency Shutdown Console

## Slide 28: III.11 SIF 059 H2S Concentration HH on Emergency Gas Scrubber (SR02) Discharge
Purpose: Detects a high concentration H2S waste gas fro 109SR02 through use
three detectors. If two detectors detect a HH reading, Emergency Gas
Scrubber Shutdown will be initiated.
Cause of SIS | SIS Action
H2S Detectors reading HH= 5ppm (2 out of 3 detectors) *Note: Operators are notified through Plant Alarm/Horn | Primary Action CLOSE Emergency Gas Scrubber Inlet Valve (109HV057/HV058)

## Slide 29: III.12 SIF 060 H2S Concentration HH on Gas Leak Scrubber (SR03) Unavailable
Purpose: Detects a high concentration H2S waste gas from 109SR02 through use
of three detectors. If two detectors detect a HH reading, Gas Leak
Scrubber Shutdown will be initiated.
Cause of SIS | SIS Action
H2S Detectors reading HH= 5ppm (2 out of 3 detectors) *Note: Operators are notified through Plant Alarm/Horn | Primary Action CLOSE Gas Leak Scrubber Inlet Valve (109HV059) STOP Fume Extraction Fan

## Slide 30: III.13 SIF 153A/253A Gas Cooler Room Gas Detector HH Trip(1)
Purpose: Prevents release of high concentration H2S gas to the atmosphere
through leaks.
Cause of SIS | SIS Action
Case 1 Gas Cooler Room Gas Detector =10ppm Gas Cooler Room Discharge Line Gas Detector =10ppm Gas Cooler Room Discharge Line Pressure Transmitter NORMAL * Note: triggered by 3 conditions | Primary Action CLOSE Gas Cooler Room Vent Valves Secondary Action OPEN Gas Cooler Room Vent to 109SR03 Valve
Alarm
  Sound the horn of H2S Core Plant to notify Operators

## Slide 31: Gas Cooler Room Gas Detector HH Trip-Case 1

## Slide 32: III.13 SIF 153A/253A Gas Cooler Room Gas Detector HH Trip(2)
Purpose: Prevents release of high concentration H2S gas to the atmosphere
through leaks.
Cause of SIS | SIS Action
Case 2 Gas Cooler Room Gas Detector =10ppm Knockout Drum Room Discharge Line Gas Detector =10ppm Gas Cooler Room Discharge Line Pressure Transmitter LL Knock-out Drum Room Discharge Line Pressure Transmitter NORMAL * Note: triggered by 3 conditions | Primary Action CLOSE Knockout Drum Room Vent Valves Secondary Action OPEN Knockout Drum Room Vent to 109SR03
Alarm
  Sound the horn of H2S Core Plant to notify Operators

## Slide 33: Gas Cooler Room Gas Detector HH Trip-Case 2

## Slide 34: III.14 SIF 153B/253B Knockout Drum Gas Detector HH Trip(1)
Purpose: Detects a gas leak within the room containing Knockout Drum. This
prevents release of high concentration H2S gas to the atmosphere
through leaks.
Cause of SIS | SIS Action
Case 1: Knockout Drum Room Gas Detector =10ppm Knock-out Drum Room Discharge Line Gas Detector =10ppm Knock-out Drum Room Discharge Line Pressure NORMAL * Note: triggered by 3 conditions | Primary Action CLOSE Knockout Drum Room Vent Valves Secondary Action OPEN Knockout Drum Vent to 109SR03
Alarm
  Sound the horn of H2S Core Plant to notify Operators

## Slide 35: Knockout Drum Room Gas Detector HH Trip-Case 1

## Slide 36: III.14 SIF 153B/253B Knockout Drum Gas Detector HH Trip(2)
Purpose: Detects a gas leak within the room containing Knockout Drum. This
prevents release of high concentration H2S gas to the atmosphere
through leaks.
Cause of SIS | SIS Action
Case 2: Knockout Drum Room Gas Detector =10ppm Gas Cooler Room Discharge Line Gas Detector =10ppm Knock-out Drum Room Discharge Line Pressure Transmitter LL Gas Cooler Room Discharge Line Pressure Transmitter NORMAL * Note: triggered by 3 conditions | Primary Action CLOSE Knockout Drum Room Vent Valves Secondary Action OPEN Gas Cooler Room Vent to 109SR03
Alarm
  Sound the horn of H2S Core Plant to notify Operators

## Slide 37: Knockout Drum Room Gas Detector HH Trip-Case 2

## Slide 38: III.15 SIF 153C/253C Quench Column Room Gas Detector HH Trip
Purpose: Detects a gas leak within the room containing Quench Column. This
prevents release of high concentration H2S gas to the atmosphere
through leaks.
Cause of SIS | SIS Action
H2S detection either one of the three Quench Column Room Area Gas Detectors= 10ppm Quench Column Room Discharge Line Gas Detector= 10ppm Quench Column Room Discharge Line Pressure Transmitter NORMAL * Note: triggered by 3 conditions | Primary Action CLOSE Quench Column Room Vent Valves Secondary Action OPEN Quench Column Room Vent Valve
Alarm
  Sound the horn of H2S Core Plant to notify Operators

## Slide 39: III.16 SIF-153G Area H2S Gas Detector High High Trip
Purpose: Detects a gas leak within the immediate Area. This prevents release of
high concentration H2S gas to the atmosphere through leaks.
Cause of SIS | SIS Action
H2S detection of Area H2S gas detectors= 10ppm | Sound the Sulfur Shelter Horn Light the Sulfur Shelter Beacon Sound the horn of H2S Core Plant Sound the Common Scrubber System Beacon Light the Common Scubber System Beacon

## Slide 40: Operator Actions when ESD Occur
HPAL Area
  In case of Power Failure, Thickeners (Ore & CCD) Rake Raise
  In case of Acid S/D, Lewa Pump Stroke set to zero and N2 addition.
  In case of Steam S/D, close main isolation valve of Blow Back Vessel
MS Area
  Closing of all feed pumps discharge valve
  Water flushing of slurry lines
  MS Thickener rake raise
  Closing of Vacuum Pump suction valve
  Closing Steam Isolation Valve at MS Feedline
H2S Area
  When ESD occurs, SIS is initiated. Operator will be notified through
  alarms (H2S Emergency Shutdown Console and/or alarm at the H2S
  Plant Core Area).
  Operator will acknowledge the buzzer alarm. Resetting the alarm can
  be done only after satisfying normal condition.